## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 4 Network Layer:
Data Plane
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
added new 8th edition material on middleboxes (and Internet arch), Net neutrality, buffering …
lighter header font
<number>

## Slide 2
Network layer: our goals
understand principles behind network layer services, focusing on data plane:
  network layer service models
  forwarding versus routing
  how a router works
  addressing
  generalized forwarding
  Internet architecture
instantiation, implementation in the Internet
  IP protocol
Network Layer: 4-2
Notes: <number>

## Slide 3
Network layer: “data plane” roadmap
Network layer: overview
  data plane
  control plane
Generalized Forwarding, SDN
  Match+action
  OpenFlow: match+action in action
Middleboxes
Network Layer: 4-3
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
Notes: <number>

## Slide 4
Network-layer services and protocols
transport segment from sending to receiving host
  sender: encapsulates segments into datagrams, passes to link layer
  receiver: delivers segments to transport layer protocol
network layer protocols in every Internet device: hosts, routers
routers:
  examines header fields in all IP datagrams passing through it
  moves datagrams from input ports to output ports to transfer datagrams along end-end path
mobile network
enterprise
network
national or global ISP
datacenter
network
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
Network Layer: 4-4
Notes: <number>

## Slide 5
Two key network-layer functions
network-layer functions:
forwarding: move packets from a router’s input link to appropriate router output link
analogy: taking a trip
forwarding: process of getting through single interchange
forwarding
routing
routing: process of planning trip from source to destination
routing: determine route taken by packets from source to destination
  routing algorithms
Network Layer: 4-5
Notes: <number>

## Slide 6
Network layer: data plane, control plane
Data plane:
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
Control plane
network-wide logic
determines how datagram is routed among routers along end-end path from source host to destination host
1
2
3
0111
values in arriving
packet header
two control-plane approaches:
  traditional routing algorithms: implemented in routers
  software-defined networking (SDN): implemented in (remote) servers
Network Layer: 4-6
Notes: <number>

## Slide 7
Per-router control plane
Individual routing algorithm components in each and every router interact in the control plane
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header
3
Network Layer: 4-7
Notes: <number>

## Slide 8
Software-Defined Networking (SDN) control plane
Remote controller computes, installs forwarding tables in routers
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header
Network Layer: 4-8
Notes: <number>

## Slide 9
Network service model
example services for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
example services for a flow of datagrams:
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing
Q: What service model for “channel” transporting datagrams from sender to receiver?
Network Layer: 4-9
Notes: <number>

## Slide 10
Network-layer service model
Network
Architecture
Internet
ATM
ATM
Internet
Internet
Service
Model
best effort
Constant Bit Rate
Available Bit Rate
Intserv Guaranteed
(RFC 1633)
Diffserv (RFC 2475)
Bandwidth
none
Constant rate
Guaranteed min
yes
possible
Loss
no
yes
no
yes
possibly
Order
no
yes
yes
yes
possibly
Timing
no
yes
no
yes
no
No guarantees on:
  successful datagram delivery to destination
  timing or order of delivery
  bandwidth available to end-end flow
Internet “best effort” service model
Quality of Service (QoS) Guarantees ?
Network Layer: 4-10
Notes: <number>

## Slide 11
Network-layer service model
Network
Architecture
Internet
ATM
ATM
Internet
Internet
Service
Model
best effort
Constant Bit Rate
Available Bit Rate
Intserv Guaranteed
(RFC 1633)
Diffserv (RFC 2475)
Bandwidth
none
Constant rate
Guaranteed min
yes
possible
Loss
no
yes
no
yes
possibly
Order
no
yes
yes
yes
possibly
Timing
no
yes
no
yes
no
Quality of Service (QoS) Guarantees ?
Network Layer: 4-11
Notes: <number>

## Slide 12
Reflections on best-effort service:
simplicity of mechanism has allowed Internet to be widely deployed adopted
sufficient provisioning of bandwidth allows performance of real-time applications (e.g., interactive voice, video) to be “good enough” for “most of the time”
replicated, application-layer distributed services (datacenters, content distribution networks) connecting close to clients’ networks, allow services to be provided from multiple locations
congestion control of “elastic” services helps
It’s hard to argue with success of best-effort service model
Network Layer: 4-12
Notes: <number>

## Slide 13
Network layer: “data plane” roadmap
Network layer: overview
  data plane
  control plane
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
Generalized Forwarding, SDN
  Match+action
  OpenFlow: match+action in action
Middleboxes
Network Layer: 4-13
Notes: <number>

## Slide 14
Router architecture overview
high-level view of generic router architecture:
high-speed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operates in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame
Network Layer: 4-14
Notes: <number>

## Slide 15
Input port functions
switch
fabric
line
termination
physical layer:
bit-level reception
link
layer
protocol
(receive)
link layer:
e.g., Ethernet
(chapter 6)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
input port queuing: if datagrams arrive faster than forwarding rate into switch fabric
Network Layer: 4-15
Notes: <number>

## Slide 16
Input port functions
line
termination
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
destination-based forwarding: forward based only on destination IP address (traditional)
generalized forwarding: forward based on any set of header field values
physical layer:
bit-level reception
switch
fabric
link
layer
protocol
(receive)
link layer:
e.g., Ethernet
(chapter 6)
Network Layer: 4-16
Notes: <number>

## Slide 17
Q: but what happens if ranges don’t divide up so nicely?
Destination-based forwarding
Network Layer: 4-17
Notes: Text for this animation:
This all works out pretty nice and looks pretty simple!
But of course the devil is in the details, as the saying goes.
What happens, for example, when a subset of addresses say in this first range should go to say interface 3, rather than interface 0. Well, of course we could split the first address range into multiple pieces, and add in this new subrange with its new destination output port. But it turns out there’s a much simpler and elegant way to do this. Known as longest prefix matching.
<number>

## Slide 18
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
********
***
********
***
********
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
11001000 00010111 00010110 10100001
Network Layer: 4-18
Notes: <number>

## Slide 19
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!
Network Layer: 4-19
Notes: <number>

## Slide 20
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!
Network Layer: 4-20
Notes: <number>

## Slide 21
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!
Network Layer: 4-21
Notes: <number>

## Slide 22
we’ll see why longest prefix matching is used shortly, when we study addressing
longest prefix matching: often performed using ternary content addressable memories (TCAMs)
  content addressable: present address to TCAM: retrieve address in one clock cycle, regardless of table size
  Cisco Catalyst: ~1M routing table entries in TCAM
Longest prefix matching
Network Layer: 4-22
Notes: <number>

## Slide 23
transfer packet from input link to appropriate output link
Switching fabrics
high-speed
switching
fabric
N input ports
N output ports
. . .
. . .
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
R
R
R
R
(rate: NR, ideally)
Network Layer: 4-23
Notes: <number>

## Slide 24
Switching fabrics
bus
memory
memory
interconnection
network
three major types of switching fabrics:
transfer packet from input link to appropriate output link
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
Network Layer: 4-24
Notes: <number>

## Slide 25
first generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
Switching via memory
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus
Network Layer: 4-25
Notes: <number>

## Slide 26
datagram from input port memory to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access routers
Switching via a bus
Network Layer: 4-26
Notes: <number>

## Slide 27
Crossbar, Clos networks, other interconnection nets initially developed to connect processors in multiprocessor
Switching via interconnection network
8x8 multistage switch
built from smaller-sized switches
3x3 crossbar
multistage switch: nxn switch from multiple stages of smaller switches
exploiting parallelism:
  fragment datagram into fixed length cells on entry
  switch cells through the fabric, reassemble datagram at exit
3x3 crossbar
Network Layer: 4-27
Notes: <number>

## Slide 28
scaling, using multiple switching “planes” in parallel:
  speedup, scaleup via parallelism
Switching via interconnection network
fabric plane 0
. . .
. . .
fabric plane 1
. . .
. . .
fabric plane 2
. . .
. . .
fabric plane 3
. . .
. . .
fabric plane 4
. . .
. . .
fabric plane 5
. . .
. . .
fabric plane 6
. . .
. . .
fabric plane 7
. . .
. . .
Cisco CRS router:
  basic unit: 8 switching planes
  each plane: 3-stage interconnection network
  up to 100’s Tbps switching capacity
Network Layer: 4-28
Notes: <number>

## Slide 29
If switch fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Input port queuing
output port contention: only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
Network Layer: 4-29
Notes: <number>

## Slide 30
Output port queuing
Buffering required when datagrams arrive from fabric faster than link transmission rate. Drop policy: which datagrams to drop if no free buffers?
Scheduling discipline chooses among queued datagrams for transmission
Datagrams can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality
This is a really important slide
line
termination
link
layer
protocol
(send)
switch
fabric
(rate: NR)
datagram
buffer
queueing
R
Network Layer: 4-30
Notes: <number>

## Slide 31
Output port queuing
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
Network Layer: 4-31
Notes: <number>

## Slide 32
RFC 3439 rule of thumb: average buffering equal to “typical” RTT (say 250 msec) times link capacity C
  e.g., C = 10 Gbps link: 2.5 Gbit buffer
How much buffering?
but too much buffering can increase delays (particularly in home routers)
  long RTTs: poor performance for realtime apps, sluggish TCP response
  recall delay-based congestion control: “keep bottleneck link just full enough (busy) but no fuller”
RTT C
.
N
more recent recommendation: with N flows, buffering equal to
Network Layer: 4-32
Notes: You might think that more buffering is a good thing. Buffering is a bit like salt—just the right amount of salt makes food better, but too much makes it inedible!
<number>

## Slide 33
Buffer Management
buffer management:
drop: which packet to add, drop when buffers are full
  tail drop: drop arriving packet
  priority: drop/remove on priority basis
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
scheduling
marking: which packets to mark to signal congestion (ECN, RED)
R
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R
Network Layer: 4-33
Notes: <number>

## Slide 34
packet scheduling: deciding which packet to send next on link
  first come, first served
  priority
  round robin
  weighted fair queueing
Packet Scheduling: FCFS
FCFS: packets transmitted in order of arrival to output port
also known as: First-in-first-out (FIFO)
real world examples?
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R
Network Layer: 4-34
Notes: <number>

## Slide 35
Priority scheduling:
arriving traffic classified, queued by class
  any header fields can be used for classification
Scheduling policies: priority
high priority queue
low priority queue
arrivals
classify
departures
link
1
3
2
4
5
arrivals
departures
packet in service
send packet from highest priority queue that has buffered packets
  FCFS within priority class
1
3
4
2
5
1
3
2
4
5
Network Layer: 4-35
Notes: <number>

## Slide 36
Round Robin (RR) scheduling:
arriving traffic classified, queued by class
  any header fields can be used for classification
Scheduling policies: round robin
classify
arrivals
departures
link
R
server cyclically, repeatedly scans class queues, sending one complete packet from each class (if available) in turn
Network Layer: 4-36
Notes: <number>

## Slide 37
Weighted Fair Queuing (WFQ):
generalized Round Robin
Scheduling policies: weighted fair queueing
classify
arrivals
departures
link
R
w1
w2
w3
wi
Sjwj
minimum bandwidth guarantee (per-traffic-class)
each class, i, has weight, wi, and gets weighted amount of service in each cycle:
Network Layer: 4-37
Notes: <number>

## Slide 38
Sidebar: Network Neutrality
What is network neutrality?
  technical: how an ISP should share/allocation its resources
  packet scheduling, buffer management are the mechanisms
  social, economic principles
    protecting free speech
    encouraging innovation, competition
  enforced legal
Different countries have different “takes” on network neutrality
Network Layer: 4-37
Notes: <number>

## Slide 39
Sidebar: Network Neutrality
2015 US FCC Order on Protecting and Promoting an Open Internet: three “clear, bright line” rules:
no blocking … “shall not block lawful content, applications, services, or non-harmful devices, subject to reasonable network management.”
no throttling … “shall not impair or degrade lawful Internet traffic on the basis of Internet content, application, or service, or use of a non-harmful device, subject to reasonable network management.”
no paid prioritization. … “shall not engage in paid prioritization”
Network Layer: 4-39
Notes: <number>

## Slide 40
ISP: telecommunications or information service?
US Telecommunication Act of 1934 and 1996:
  Title II: imposes “common carrier duties” on telecommunications services: reasonable rates, non-discrimination and requires regulation
  Title I: applies to information services:
    no common carrier duties (not regulated)
    but grants FCC authority “… as may be necessary in the execution of its functions”
Is an ISP a “telecommunications service” or an “information service” provider?
the answer really matters from a regulatory standpoint!
Network Layer: 4-40
Notes: <number>

## Slide 41
Network layer: “data plane” roadmap
Network layer: overview
  data plane
  control plane
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
Generalized Forwarding, SDN
  match+action
  OpenFlow: match+action in action
Middleboxes
Network Layer: 4-41
Notes: <number>

## Slide 42
Network Layer: Internet
host, router network layer functions:
IP protocol
datagram format
addressing
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer
forwarding
table
Path-selection algorithms: implemented in
routing protocols (OSPF, BGP)
SDN controller
Network Layer: 4-41
Notes: <number>

## Slide 43
IP Datagram format
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
IP protocol version number
header length(bytes)
upper layer protocol (e.g., TCP or UDP)
total datagram
length (bytes)
“type” of service:
diffserv (0:5)
ECN (6:7)
fragmentation/
reassembly
TTL: remaining max hops
(decremented at each router)
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead for TCP+IP
overhead
e.g., timestamp, record route taken
32-bit source IP address
32-bit destination IP address
header checksum
Maximum length: 64K bytes
Typically: 1500 bytes or less
Network Layer: 4-41
Notes: <number>

## Slide 44
network links have MTU (max. transfer size) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at destination
  IP header bits used to identify, order related fragments
IP fragmentation/reassembly
Network Layer: 4-44
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…
Notes: <number>

## Slide 45
IP fragmentation/reassembly
Network Layer: 4-44
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8
Notes: <number>

## Slide 46
IP address: 32-bit identifier associated with each host or router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
IP addressing: introduction
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
dotted-decimal IP address notation:
Network Layer: 4-46
Notes: <number>

## Slide 47
IP address: 32-bit identifier associated with each host or router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
IP addressing: introduction
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
dotted-decimal IP address notation:
Network Layer: 4-<number>
Notes: <number>

## Slide 48
IP addressing: introduction
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
Q: how are interfaces actually connected?
A: wired
Ethernet interfaces connected by Ethernet switches
A: wireless WiFi interfaces connected by WiFi base station
For now: don’t need to worry about how one interface is connected to another (with no intervening router)
A: we’ll learn about that in chapters 6, 7
Network Layer: 4-<number>
Notes: <number>

## Slide 49
Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
What’s a subnet ?
  device interfaces that can physically reach each other without passing through an intervening router
network consisting of 3 subnets
IP addresses have structure:
  subnet part: devices in same subnet have common high order bits
  host part: remaining low order bits
Network Layer: 4-<number>
Notes: <number>

## Slide 50
Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
Recipe for defining subnets:
detach each interface from its host or router, creating “islands” of isolated networks
each isolated network is called a subnet
subnet mask: /24
(high-order 24 bits: subnet part of IP address)
subnet
223.1.3.0/24
subnet 223.1.1.0/24
subnet 223.1.2.0/24
Network Layer: 4-<number>
Notes: <number>

## Slide 51
Subnets
where are the subnets?
what are the /24 subnet addresses?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
223.1.2.1
subnet 223.1.1/24
subnet 223.1.7/24
subnet 223.1.3/24
subnet 223.1.2/24
subnet 223.1.9/24
subnet 223.1.8/24
Network Layer: 4-<number>
Notes: <number>

## Slide 52
IP addressing: CIDR
CIDR: Classless InterDomain Routing (pronounced “cider”)
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
Network Layer: 4-<number>
Notes: <number>

## Slide 53
IP addresses: how to get one?
That’s actually two questions:
Q: How does a host get IP address within its network (host part of address)?
Q: How does a network get IP address for itself (network part of address)
How does host get IP address?
hard-coded by sysadmin in config file (e.g., /etc/rc.config in UNIX)
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”
Network Layer: 4-<number>
Notes: <number>

## Slide 54
DHCP: Dynamic Host Configuration Protocol
goal: host dynamically obtains IP address from network server when it “joins” network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/on)
  support for mobile users who join/leave network
DHCP overview:
  host broadcasts DHCP discover msg [optional]
  DHCP server responds with DHCP offer msg [optional]
  host requests IP address: DHCP request msg
  DHCP server sends address: DHCP ack msg
Network Layer: 4-<number>
Notes: <number>

## Slide 55
DHCP client-server scenario
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
DHCP server
223.1.2.5
arriving DHCP client needs
address in this network
Typically, DHCP server will be co-located in router, serving all subnets to which router is attached
Network Layer: 4-<number>
Notes: <number>

## Slide 56
DHCP client-server scenario
DHCP server: 223.1.2.5
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I would like to use this IP address!
Broadcast: OK. You’ve got that IP address!
The two steps above can be skipped “if a client remembers and wishes to reuse a previously allocated network address” [RFC 2131]
Network Layer: 4-<number>
Notes: <number>

## Slide 57
DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)
Network Layer: 4-<number>
Notes: <number>

## Slide 58
DHCP: example
Connecting laptop will use DHCP to get IP address, address of first-hop router, address of DNS server.
router with DHCP
server built into
router
DHCP REQUEST message encapsulated in UDP, encapsulated in IP, encapsulated in Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demux’ed to IP demux’ed, UDP demux’ed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
Network Layer: 4-<number>
Notes: <number>

## Slide 59
DHCP: example
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulated DHCP server reply forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DNS server, IP address of its first-hop router
Network Layer: 4-<number>
Notes: <number>

## Slide 60
IP addresses: how to get one?
Q: how does network get subnet part of IP address?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
ISP can then allocate out its address space in 8 blocks:
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23
Network Layer: 4-<number>
Notes: <number>

## Slide 61
Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
hierarchical addressing allows efficient advertisement of routing information:
Network Layer: 4-<number>
Notes: <number>

## Slide 62
Hierarchical addressing: more specific routes
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
200.23.18.0/23
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Organization 1 moves from Fly-By-Night-ISP to ISPs-R-Us
ISPs-R-Us now advertises a more specific route to Organization 1
200.23.18.0/23
Organization 1
“or 200.23.18.0/23”
Network Layer: 4-<number>
Notes: <number>

## Slide 63
Hierarchical addressing: more specific routes
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Organization 1 moves from Fly-By-Night-ISP to ISPs-R-Us
ISPs-R-Us now advertises a more specific route to Organization 1
200.23.18.0/23
Organization 1
“or 200.23.18.0/23”
Network Layer: 4-<number>
Notes: <number>

## Slide 64
IP addressing: last words ...
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned Names and Numbers http://www.icann.org/
  allocates IP addresses, through 5 regional registries (RRs) (who may then allocate to local registries)
  manages DNS root zone, including delegation of individual TLD (.com, .edu , …) management
Q: are there enough 32-bit IP addresses?
ICANN allocated last chunk of IPv4 addresses to RRs in 2011
NAT (next) helps IPv4 address space exhaustion
IPv6 has 128-bit address space
"Who the hell knew how much address space we needed?" Vint Cerf (reflecting on decision to make IPv4 address 32 bits long)
Network Layer: 4-<number>
Notes: <number>

## Slide 65
Network layer: “data plane” roadmap
Network layer: overview
  data plane
  control plane
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
Generalized Forwarding, SDN
  match+action
  OpenFlow: match+action in action
Middleboxes
Network Layer: 4-<number>
Notes: <number>

## Slide 66
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
local network (e.g., home network) 10.0.0/24
138.76.29.7
rest of
Internet
NAT: network address translation
datagrams with source or destination in this network have 10.0.0/24 address for source, destination (as usual)
all datagrams leaving local network have same source NAT IP address: 138.76.29.7, but different source port numbers
NAT: all devices in local network share just one IPv4 address as far as outside world is concerned
Network Layer: 4-<number>
Notes: <number>

## Slide 67
  all devices in local network have 32-bit addresses in a “private” IP address space (10/8, 172.16/12, 192.168/16 prefixes) that can only be used in local network
  advantages:
    just one IP address needed from provider ISP for all devices
    can change addresses of host in local network without notifying outside world
    can change ISP without changing addresses of devices in local network
    security: devices inside local net not directly addressable, visible by outside world
NAT: network address translation
Network Layer: 4-<number>
Notes: <number>

## Slide 68
implementation: NAT router must (transparently):
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
      remote clients/servers will respond using (NAT IP address, new port #) as destination address
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in destination fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table
NAT: network address translation
Network Layer: 4-<number>
Notes: <number>

## Slide 69
NAT: network address translation
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1 sends datagram to 128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router changes datagram source address from 10.0.0.1, 3345 to 138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives, destination address: 138.76.29.7, 5001
10.0.0.1
10.0.0.2
10.0.0.3
Network Layer: 4-<number>
Notes: <number>

## Slide 70
NAT has been controversial:
  routers “should” only process up to layer 3
  address “shortage” should be solved by IPv6
  violates end-to-end argument (port # manipulation by network-layer device)
  NAT traversal: what if client wants to connect to server behind NAT?
but NAT is here to stay:
  extensively used in home and institutional nets, 4G/5G cellular nets
NAT: network address translation
Network Layer: 4-<number>
Notes: <number>

## Slide 71
initial motivation: 32-bit IPv4 address space would be completely allocated
additional motivation:
  speed processing/forwarding: 40-byte fixed length header
  enable different network-layer treatment of “flows”
IPv6: motivation
Network Layer: 4-<number>
Notes: <number>

## Slide 72
IPv6 datagram format
payload (data)
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
priority: identify priority among datagrams in flow
flow label: identify datagrams in same "flow.” (concept of “flow” not well defined).
128-bit
IPv6 addresses
What’s missing (compared with IPv4):
no checksum (to speed processing at routers)
no fragmentation/reassembly
no options (available as upper-layer, next-header protocol at router)
Network Layer: 4-<number>
Notes: <number>

## Slide 73
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
Transition from IPv4 to IPv6
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers (“packet within a packet”)
  tunneling used extensively in other contexts (4G/5G)
Network Layer: 4-<number>
Notes: <number>

## Slide 74
Tunneling and encapsulation
Ethernet connecting two IPv6 routers:
Ethernet connects two IPv6 routers
A
B
IPv6
IPv6
E
F
IPv6
IPv6
Link-layer frame
IPv6 datagram
The usual: datagram as payload in link-layer frame
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
IPv4 network
IPv4 network connecting two IPv6 routers
Network Layer: 4-<number>
Notes: <number>

## Slide 75
Tunneling and encapsulation
Ethernet connecting two IPv6 routers:
Ethernet connects two IPv6 routers
A
B
IPv6
IPv6
E
F
IPv6
IPv6
IPv4 tunnel connecting two IPv6 routers
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
E
F
IPv6
Link-layer frame
IPv6 datagram
The usual: datagram as payload in link-layer frame
IPv4 datagram
IPv6 datagram
tunneling: IPv6 datagram as payload in a IPv4 datagram
IPv6/v4
IPv6/v4
Network Layer: 4-<number>
Notes: <number>

## Slide 76
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
Tunneling
physical view:
IPv4
IPv4
E
IPv6/v4
IPv6
F
C
D
A
B
IPv6
IPv6/v4
logical view:
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
Note source and destination addresses!
Network Layer: 4-<number>
Notes: <number>

## Slide 77
Google1: ~ 30% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
IPv6: adoption
1 https://www.google.com/intl/en/ipv6/statistics.html
Network Layer: 4-<number>
Notes: <number>

## Slide 78
Google1: ~ 30% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
Long (long!) time for deployment, use
  25 years and counting!
  think of application-level changes in last 25 years: WWW, social media, streaming media, gaming, telepresence, …
  Why?
IPv6: adoption
1 https://www.google.com/intl/en/ipv6/statistics.html
Network Layer: 4-<number>
Notes: <number>

## Slide 79
Network layer: “data plane” roadmap
Network layer: overview
  data plane
  control plane
Generalized Forwarding, SDN
  Match+action
  OpenFlow: match+action in action
Middleboxes
Network Layer: 4-<number>
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
Notes: <number>

## Slide 80
1
2
0111
3
values in arriving
packet header
Generalized forwarding: match plus action
Review: each router contains a forwarding table
“match plus action” abstraction: match bits in arriving packet, take action
  generalized forwarding:
    many header fields can determine action
    many action possible: drop/copy/modify/log packet
forwarding table
(aka: flow table)
(aka: flow table)
  destination-based forwarding: forward based on dest. IP address
Network Layer: 4-<number>
Notes: <number>

## Slide 81
flow: defined by header field values (in link-, network-, transport-layer fields)
generalized forwarding: simple packet-handling rules
  match: pattern values in packet header fields
  actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  priority: disambiguate overlapping patterns
  counters:
Flow table abstraction
Router’s flow table define router’s match+action rules
Flow table
match
action
Network Layer: 4-<number>
Notes: <number>

## Slide 82
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  match: pattern values in packet header fields
  actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  priority: disambiguate overlapping patterns
  counters: #bytes and #packets
Flow table
match
action
1
2
3
4
* : wildcard
src=10.1.2.3, dest=*.*.*.* send to controller
src=1.2.*.*, dest=*.*.*.* drop
src = *.*.*.*, dest=3.4.*.* forward(2)
Flow table abstraction
Network Layer: 4-<number>
Notes: <number>

## Slide 83
OpenFlow: flow table entries
Match
Action
Stats
Forward packet to port(s)
Drop packet
Modify fields in header(s)
Encapsulate and forward to controller
Packet + byte counters
Header fields to match:
Ingress Port
Src MAC
Dst MAC
Eth Type
VLAN
ID
IP
ToS
IP Proto
IP Src
IP Dst
TCP/UDP Src Port
VLAN
Pri
TCP/UDP Dst Port
Link layer
Network layer
Transport layer
Network Layer: 4-<number>
Notes: <number>

## Slide 84
OpenFlow: examples
IP datagrams destined to IP address 51.6.0.8 should be forwarded to router output port 6
Block (do not forward) all datagrams destined to TCP port 22 (ssh port #)
Block (do not forward) all datagrams sent by host 128.119.1.1
Destination-based forwarding:
*
*
*
*
*
*
51.6.0.8
*
*
*
port6
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
*
*
*
*
*
*
*
*
*
*
*
*
Firewall:
drop
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
22
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
*
*
*
*
*
*
*
*
*
*
drop
*
128.119.1.1
Network Layer: 4-<number>
Notes: <number>

## Slide 85
OpenFlow: examples
Layer 2 destination-based forwarding:
layer 2 frames with destination MAC address 22:A7:23:11:E1:02 should be forwarded to output port 3
*
*
*
*
*
*
*
*
*
port3
22:A7:23:
11:E1:02
*
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
Network Layer: 4-<number>
Notes: <number>

## Slide 86
match+action: abstraction unifies different kinds of devices
OpenFlow abstraction
Router
  match: longest destination IP prefix
  action: forward out a link
Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port
Network Layer: 4-<number>
Notes: <number>

## Slide 87
OpenFlow example
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Orchestrated tables can create network-wide behavior, e.g.,:
datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2
Network Layer: 4-<number>
Notes: <number>

## Slide 88
OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Orchestrated tables can create network-wide behavior, e.g.,:
datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2
Network Layer: 4-<number>
Notes: <number>

## Slide 89
Generalized forwarding: summary
“match plus action” abstraction: match bits in arriving packet header(s) in any layers, take action
  matching over many fields (link-, network-, transport-layer)
  local actions: drop, forward, modify, or send matched packet to controller
  “program” network-wide behaviors
simple form of “network programmability”
  programmable, per-packet “processing”
  historical roots: active networking
  today: more generalized programming:
P4 (see p4.org).
Network Layer: 4-<number>
Notes: <number>

## Slide 90
Network layer: “data plane” roadmap
Network Layer: 4-<number>
Network layer: overview
What’s inside a router
IP: the Internet Protocol
Generalized Forwarding
Middleboxes
  middlebox functions
  evolution, architectural principles of the Internet
Notes: <number>

## Slide 91
Middleboxes
“any intermediary box performing functions apart from normal, standard functions of an IP router on the data path between a source host and destination host”
Middlebox (RFC 3234)
Notes: <number>

## Slide 92
Middleboxes everywhere!
enterprise
network
national or global ISP
datacenter
network
NAT: home, cellular, institutional
Firewalls, IDS: corporate, institutional, service providers, ISPs
Load balancers: corporate, service provider, data center, mobile nets
Caches: service provider, mobile, CDNs
Application-specific: service providers, institutional, CDN

## Slide 93
Middleboxes
initially: proprietary (closed) hardware solutions
move towards “whitebox” hardware implementing open API
  move away from proprietary hardware solutions
  programmable local actions via match+action
  move towards innovation/differentiation in software
SDN: (logically) centralized control and configuration management often in private/public cloud
network functions virtualization (NFV): programmable services over white box networking, computation, storage
Notes: <number>

## Slide 94
The IP hourglass
IP
TCP
UDP
HTTP
SMTP
QUIC
DASH
RTP
…
Ethernet
WiFi
Bluetooth
PPP
PDCP
…
copper radio fiber
Internet’s “thin waist”:
one network layer protocol: IP
must be implemented by every (billions) of Internet-connected devices
many protocols in physical, link, transport, and application layers
Notes: <number>

## Slide 95
The IP hourglass, at middle age
IP
TCP
UDP
HTTP
SMTP
QUIC
DASH
RTP
…
Ethernet
WiFi
Bluetooth
PPP
PDCP
…
copper radio fiber
Internet’s middle age “love handles”?
middleboxes, operating inside the network
NAT
NFV
Firewalls
caching
Notes: <number>

## Slide 96
Architectural Principles of the Internet
“Many members of the Internet community would argue that there is no architecture, but only a tradition, which was not written down for the first 25 years (or at least not by the IAB). However, in very general terms, the community believes that
RFC 1958
the goal is connectivity, the tool is the Internet Protocol, and the intelligence is end to end rather than hidden in the network.”
Three cornerstone beliefs:
simple connectivity
IP protocol: that narrow waist
intelligence, complexity at network edge
Notes: <number>

## Slide 97
The end-end argument
some network functionality (e.g., reliable data transfer, congestion) can be implemented in network, or at network edge
end-end implementation of reliable data transfer
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
hop-by-hop (in-network) implementation of reliable data transfer
Notes: <number>

## Slide 98
The end-end argument
“The function in question can completely and correctly be implemented only with the knowledge and help of the application standing at the end points of the communication system. Therefore, providing that questioned function as a feature of the communication system itself is not possible. (Sometimes an incomplete version of the function provided by the communication system may be useful as a performance enhancement.)
We call this line of reasoning against low-level function implementation the “end-to-end argument.”
Saltzer, Reed, Clark 1981
some network functionality (e.g., reliable data transfer, congestion) can be implemented in network, or at network edge
Notes: <number>

## Slide 99
Where’s the intelligence?
20th century phone net:
intelligence/computing at network switches
Internet (pre-2005)
intelligence, computing at edge
Internet (post-2005)
programmable network devices
intelligence, computing, massive application-level infrastructure at edge
Notes: The 20th century phone network had dumb network endpoints, really by definition. The end points were rotary phones that maybe only your parents and grandparents remember; they weren’t computers. They really were dumb devices, and therefore the phone network had programmable switches that were quite smart. All functionality – well, all of the intelligence - was implemented within the network. It HAD to be. The end systems could not do anything more than send digits and send audio signals.
When the Internet came along, the endpoints and the switches were both programmable computers. So where to put the complexity? RFC 1958 – the architectural principles of the Internet RFC - that says “intelligence is end to end rather than hidden in the network.” That puts the intelligence clearly at the edge, like we see here. And that’s possible because the edge devices are smart; they’re programmable. Well that’s the diagram as I remember it 20 years ago.
And in the 20 years since, as we see the rise of middleboxes and SDN, we’re now seeing intelligence (in software) layered on top of “dumb” whiteboxes within the network. So I might add a brain here today. And with datacenters and content distribution networks, we see even smarter and more sophisticated application-level infrastructure being connected at points within the network. So now there are clearly much much bigger, much more computationally intensive and complex, endpoints if you will in today’s Internet
<number>

## Slide 100
Question: how are forwarding tables (destination-based forwarding) or flow tables (generalized forwarding) computed?
Answer: by the control plane (next chapter)
Chapter 4: done!
Generalized Forwarding, SDN
Middleboxes
Network layer: overview
What’s inside a router
IP: the Internet Protocol

## Slide 101
Additional Chapter 4 slides
Network Layer: 4-<number>
Notes: <number>

## Slide 102
network links have MTU (max. transfer size) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at destination
  IP header bits used to identify, order related fragments
IP fragmentation/reassembly
Network Layer: 4-<number>
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…
Notes: <number>

## Slide 103
IP fragmentation/reassembly
Network Layer: 4-<number>
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8
Notes: <number>

## Slide 104
DHCP: Wireshark output (home LAN)
Network Layer: 4-<number>
Message type: Boot Reply (2)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 192.168.1.101 (192.168.1.101)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 192.168.1.1 (192.168.1.1)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP ACK
Option: (t=54,l=4) Server Identifier = 192.168.1.1
Option: (t=1,l=4) Subnet Mask = 255.255.255.0
Option: (t=3,l=4) Router = 192.168.1.1
Option: (6) Domain Name Server
Length: 12; Value: 445747E2445749F244574092;
IP Address: 68.87.71.226;
IP Address: 68.87.73.242;
IP Address: 68.87.64.146
Option: (t=15,l=20) Domain Name = "hsd1.ma.comcast.net."
Message type: Boot Request (1)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 0.0.0.0 (0.0.0.0)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 0.0.0.0 (0.0.0.0)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP Request
Option: (61) Client identifier
Length: 7; Value: 010016D323688A;
Hardware type: Ethernet
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Option: (t=50,l=4) Requested IP Address = 192.168.1.101
Option: (t=12,l=5) Host Name = "nomad"
Option: (55) Parameter Request List
Length: 11; Value: 010F03062C2E2F1F21F92B
1 = Subnet Mask; 15 = Domain Name
3 = Router; 6 = Domain Name Server
44 = NetBIOS over TCP/IP Name Server
……
reply
request
Notes: <number>